On the general point of view, the whole work flow is an iterative process based on :

1. search for the strongest peaks
2. autoindexing those peaks
3. refining offsets
4. filter unwanted peaks
5. build shape library
6. predict new peaks
7. integrate peaks
8. statistics

the steps 2. to 7. being repeated until you good statistics

AutoIndexing workflow :
1. Compute directions with the highest periodicity based on a discretized unit sphere in Q-space
2. Produce basis based on triplets of these directions
3. Refine the basis without any constraints
4. Reduce those basis to Niggli (pri mitive) cell
5. Reduce the Niggli cell to Gruber (conventional) cell → UB
6. Refine the unit cell with constraints on B

Build shape library:

1. Take the peak part of the integration region of each peak
2. Substract to it the average background corresponding to its background region
3. Make a 3D histogram out of this background substracted peak → 3D profile
  based on this we can predict peaks as follows
4. Select a coordinate in detector space (px,py,frame)
5. Take the average of the surrounding 3D profiles → predicted profile P
Integration :

pixel sum aka strong peak integration

1. Predict the profile for a given peak located at [h k l]BU
2. From that profile get the average covariance matrix
3. Use the same integration technique as for peak find algorithm

other methods use a model for measured intensities M which is defined as

Mi = I*Pi + B for each index of the predicted peak profiles

I and B are obtained by minimizing chi-square defied as :

%chi ^{2} = sum from{i} { { (M_{i}-IP_{i}-B)^2 } over {%alpha_i^{2}}}